| Type | 4JB1 | 4JB1T |
| --- | --- | --- |
| Bore x stroke |  | 93mm x 102mm |
| Type | 4 stroke, water cooling, inline, direct injection combustion chamber |
| Displacement | 2.771L |
| Compression ratio |  | 18.2 : 1 |
| Ignition order | 1-3-4-2 |
| Lubricating method | Forced and Splash lubrication |
| Rated power/speed | 57 kw /3,600 rpm | 68kw/3,600rpm |
| Max torque/speed | 172 N .m /2,000rpm | 200 N .m /2,000rpm |
| Output per litre | 20.6kw/L | 24.5kw/L |
| Min fuel consumption | ≤221 g/kw.h |

| Item | 4JB1/4JB1T Engine |
| --- | --- |
| Dimensions (L * W * H) | 850*630*750 MM |
| Volume per set | 0.41 M3 |
| Gross weight | 255/265 KG |
| Net weight | 230/245 KG |
| Packing | Plastic bag + steel bracket + paper carton |
| 20# Container Load 5.9*2.32*2.32（m） | 63 SET |

| Type | 4JA1 |
| --- | --- |
| Bore x stroke | 93mm x 92mm |
| Type | 4 stroke, water cooling, inline, direct injection combustion chamber |
| Displacement | 2.449L |
| Compression ratio | 18.4 : 1 |
| Ignition order | 1-3-4-2 |
| Lubricating method | Forced and Splash lubrication |
| Rated power/speed | 50 kw /3,600 rpm |
| Max torque/speed | 176 N .m /2,000rpm |
| Min fuel consumption | ≤231 g/kw.h |

| Item | Unit | 4JA1 Engine |
| --- | --- | --- |
| Dimensions (L * W * H) | mm | 850*630*750 |
| Volume per set | M3 | 0.41 |
| Gross weight | Kg | 255/265 |
| Net weight | Kg | 230/245 |
| Packing | Plastic bag + steel bracket + paper carton |
| 20# Container Load 5.9*2.32*2.32（m） | set | 63 |

ISUZU 4BD1 AND 4BD1T DIESEL ENGINE

The main technical parameters of ISUZU ENGINE Model 4BD1 4BD1T Type Vertical, in-line, water-cooled, four strokes natural aspirated turbo-charging No. of cylinder-bore×stroke 4—102×118 Displacement 3.856 Type of combustion chamber Direct injection, square combustion chamber Compression ratio 17.5:1 16.5:1 Rated power/speed (KW/r/min) 70.6/3200 88/2800 Max torque/speed(N·m/r/min) 245/2200 324/1400-1800 Full load min.fuel consumption 216 209 Max. idling speed 3520 3080 Idling steady speed ≤650 Firing order 1-3-4-2 1-3-4-2 Emission standard Euro II Net weight 330 340 Overall dimension(L×W×H)mm 921×651×751 810×660×813 Application 1.5-3 tons cargo truck, JAC light-duty truck

the main technical parameters of ISUZU 6BD1 and 6BD1T Model 6BD1 6BD1T Type Vehicle, in-line, water-cooled, four- stroke natural aspirated turbo-charging No. of cylinder-bore×stroke 6- 102 X 118 Displacement 5.785 Type of combustion chamber direct injection, square combustion chamber Compression ratio 17.5:1 16.5:1 Rated power/speed (KW/r/min) 103（140Ps）/3000 120/2800 Max torque/speed(N·m/r/min) 372/2000 460/1400－1800 Full load min.fuel onsumption 231.2 220 224.4 ≤220 Max. idling speed 3250 3240 3024 3080 Idling steady speed ≤650 700－750 Oil & fuel consumption percent ratio % ≤0.3 Firing order 1-5-3-6-2-4 Emission standard EuroⅠ Net weight 480 495 Overall dimension(L×W×H)mm 1220x640x1020 1240×700×970 Application Apply for medium-ton trucks, high-grade intercity buses, Luxury tourist buses and also serves for other machineries by modification. The main technical parameters of 4HE1T Model 4HE1T Type Vehicle, in-line, water-cooled, four strokes, supercharged inter-cool No. of cylinder-bore×stroke 4—110×125 Displacement 4.752 Type of combustion chamber Direct injection, circular beading combustion chamber Compression ratio 18:1 Rated power/speed (KW/r/min) 120/2600 115/2600 125/2300 Max torque/speed(N·m/r/min) 520/1400-1600 450/1400-1600 585/1300-1500 Full load min.fuel onsumption ≤210 Max. idling speed 2990, 2860, 2530-2645 Idling steady speed 700－750 Oil & fuel consumption percent ratio % ≤0.5 Firing order 1-3-4-2 Emission standard EuroII Net weight 395 Overall dimension(L×W×H)mm 1181×699.8×833.3

| The main technical parameters of 4HE1T |
| --- |
| Model | 4HE1T |
| Type | Vehicle, in-line, water-cooled, four strokes, supercharged inter-cool |
| No. of cylinder-bore×stroke | 4—112×125 |
| Displacement | 4.334 |
| Type of combustion chamber | Direct injection, circular beading combustion chamber |
| Compression ratio | 18.5:1 |
| Rated power/speed (KW/r/min) | 110/2600 |
| Max torque/speed(N·m/r/min) | 450/1400-1500 |
| Full load min.fuel onsumption | ≤225 |
| Max. idling speed | 3090 |
| Idling steady speed | ≤750 |
| Oil & fuel consumption percent ratio % | ≤0.6 |
| Firing order | 1-3-4-2 |
| Emission standard | EuroII |
| Net weight | 395 |
| Overall dimension(L×W×H)mm | 1121.5×615.5×743.5 |

ISUZU 4HK1-TC DIESEL ENGINE

ENGINE MODEL ISUZU 4HK1 ISUZU 4HK1-TC No-bore×stroke（mm） 4-115×125 compressor ratio 18.5 18.5 chamble shape ω ω valve type tope,4valve tope,4valve dimension(mm) 876×859×928 876×859×928 net weight（kg） 400 400 displacement（L） 5.193 5.193 engine power(kW/r/min) 110/3200 128/3200 max torque（N.m/r/min) 402/2000 500/2000 full loading speed(r/min) 2800 3000 max idle speed(r/min) 3200 3400 min fuel consumptiong/kW.h)/r/min 205 205

| ENGINE MODEL | 6HK1 | 6HK1-TC |
| --- | --- | --- |
| No-bore×stroke（mm） | 6-115×125 |
| compressor ratio | 17.5 | 16.9 |
| chamble shape | ω | ω |
| valve type | tope,4valve | tope,4valve |
| dimension(mm) | 1314×859×928 | 1312×891×984 |
| net weight（kg） | 614 | 625 |
| displacement（L） | 7.79 | 7.79 |
| engine power(kW/r/min) | 169/2700 | 191/2500 |
| max torque（N.m/r/min) | 667/1700 | 740/1500 |
| full loading speed(r/min) | 2800 | 2600 |
| max idle speed(r/min) | 3200 | 2860 |
| min fuel consumptiong/kW.h)/r/min | 218 | 218 |