Perkins phaser series engine is a reliable, powerful and fuel-saving engine for automotives

Phaser unit pump series.

| Engine Model | Phaser110Ti-S30 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled,Vertical Inline, DirectInjection, Dry Liner |
| Cylinder Number | 4 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 3.99 |
| Firing Order | 1-3-4-2 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 81/2500 |
| Max. Torque/Speed (N.m/rpm) | 360/（1400-1600） |
| Emission | EuroIII |

| Engine Model | Phaser135Ti-S30 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline,Direct Injection, Dry Liner |
| Cylinder Number | 4 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 3.99 |
| Firing Order | 1-3-4-2 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 101/2500 |
| Max. Torque/Speed (N.m/rpm) | 460/（1400-1600） |
| Emission | EuroIII |

| Engine Model | Phaser160Ti-S30 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline, DirectInjection, Dry Liner |
| Cylinder Number | 6 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 17.5:1 |
| Power/Speed (kW/rpm) | 118/2500 |
| Torque/Speed (N.m/rpm) | 555/（1400-1600） |
| Emission | EuroIII |

| Engine Model | Phaser180Ti-S30 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline, DirectInjection, Dry Liner |
| Cylinder Number | 6 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 134/2500 |
| Max. Torque/Speed (N.m/rpm) | 640/（1400-1600） |
| Emission | EuroIII |

| Engine Model | Phaser210Ti-S30 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline, DirectInjection, Dry Liner |
| Cylinder Number | 6 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 156/2500 |
| Max. Torque/Speed (N.m/rpm) | 737/（1400-1600） |
| Emission | EuroIII |

Phaser Common rail series

| Engine Model | Phaser140Ti-E30/40 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline, Direct Injection,Dry Liner |
| Cylinder Number | 4 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 3.99 |
| Firing Order | 1-3-4-2 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 104/2500 |
| Max. Torque/Speed (N.m/rpm) | 445/（1400-1600） |
| Emission | EuroIII |

| Engine Model | Phaser210Ti-E30/40 |
| --- | --- |
| Model Information | Four-Stroke, Liquid Cooled, Vertical Inline, Direct Injection,Dry Liner |
| Cylinder Number | 6 |
| Induction system | Tubrocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 17.5:1 |
| Rated Power/Speed (kW/rpm) | 156/2500 |
| Max. Torque/Speed (N.m/rpm) | 737/（1400-1600） |
| Emission | EuroIII |

Phaser natural gas series

| Engine Model | Phaser110TiN-30/40 |
| --- | --- |
| Cylinder Number | 4 |
| Induction System | Turbocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 3.99 |
| Firing Order | 1-3-4-2 |
| Compression Ratio | 10.3:1 |
| Power/Speed (kW/rpm) | 81/2600 |
| Torque/Speed (N.m/rpm) | 360/1600 |
| Noise dB(A) | ≤92 |
| Dimensions (mm) L×W×H | 890×826×844 |
| kg) (engine without packing) | 458 |
| Emission | EuroⅢ/Ⅳ |

| Engine Model | Phaser135TiN-30/40 |
| --- | --- |
| Cylinder Number | 4 |
| Induction System | Turbocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 3.99 |
| Firing Order | 1-3-4-2 |
| Compression Ratio | 10.3:1 |
| Rated Power/Speed (kW/rpm) | 101/2600 |
| Max. Torque/Speed (N.m/rpm) | 445/1600 |
| Noise dB(A) | ≤92 |
| Dimensions (mm) L×W×H | 890×826×844 |
| Weight (kg) (engine without | 458 |
| packing)Emission | EuroⅢ/Ⅳ |

| Engine Model | Phaser180TiN-30/40 |
| --- | --- |
| Cylinder Number | 6 |
| Induction System | Turbocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 10.3:1 |
| Rated Power/Speed (kW/rpm) | 134/2600 |
| Max. Torque/Speed (N.m/rpm) | 640/1600 |
| Noise dB(A) | ≤94 |
| Dimensions (mm) L×W×H | 1175×796×850 |
| Weight (kg) (engine without packing) | 578 |
| Emission | EuroⅢ/Ⅳ |

| Engine Model | Phaser210TiN-30/40 |
| --- | --- |
| Cylinder Number | 6 |
| Induction System | Turbocharged & Intercooled |
| Bore x Stroke (mm) | 100×127 |
| Displacement (L) | 5.99 |
| Firing Order | 1-5-3-6-2-4 |
| Compression Ratio | 10.3:1 |
| Rated Power /Speed(kW/rpm) | 156/2600 |
| Max. Torque/Speed (N.m/rpm) | 740/1600 |
| Noise dB(A) | ≤94 |
| Dimensions (mm) L×W×H | 1175×796×850 |
| Weight (kg) (engine without packing) | 578 |
| Emission | EuroⅢ/Ⅳ |